## Slide 1: Design of an Efficient Multicast Protocol for IEEE 802.11n WLANs
Ahmed Mehfooz, Amna Abid, Shanzae Nadeem Khan

## Slide 2: The Future of Online Video Traffic: Predictions by Cisco
“By 2018, IP video will represent 79% percent of all internet traffic, up from 66% in 2013”
“75% of Internet traffic will be accessed via WiFi by 2018”

## Slide 3: Why Multicast?
Unicast transmissions are inefficient for delivery of duplicate packets
Multicast concurrently broadcasts one packet to multiple destinations – an efficient alternative to reduce unnecessary packet duplications

## Slide 4: Multicast in 802.11n
Broadcast multicast packets at the base rate
Transmits a single frame only
Receivers do not provide feedback for packets sent to them

## Slide 5: What is Multicast in 802.11n missing out on?
High transmission rates
  up to 300 Mbps
Reliability
  due to ACKs
Frame Aggregation
  multiple frames in a single aggregate frame

## Slide 6: Challenges in Multicast for 802.11n
High Transmission rates make it tough for receivers with poor link quality to correctly receive packets
Feedback provides substantive overhead
  may degrade system throughput
  frame aggregation becomes difficult

## Slide 7: Related Works
Multicast
Protocols
Leader-based
DPMM(Double Piggyback Mode Multicast)
ACK-Based
Non-leader-Based
ACK-Based
NACK-Based
NACK-Based
REMP(Reliable and efficient Multicast Protocol)
BMMM(Batch Mode Multicast MAC Protocol)
Only in Leader Based Protocols
(e.g.)
(e.g.)
(e.g.)
(e.g.)

## Slide 8: Leader-Based Multicast Protocols
Leader Selection
  Usually the node with the worst link quality
Leader is responsible for sending feedback on behalf of the group

## Slide 9: Advantages of Leader-Based approach
Control frame overhead is minimal
Reduced number of contention phases
Enables frame aggregation

## Slide 10: Problems with Leader-Based approach
Leader Selection can add substantive overhead, a new leader is selected when:
  A new node joins the group
  A leader node leaves the group
  A loss occurs
Leader’s feedback not always representative of the group

## Slide 11: BMMM (Batch Mode Multicast MAC Protocol)
Sender uses RTS frames to sequentially instruct each intended receiver to transmit a CTS
To coordinate the ACK transmissions Request for ACK(RAK) is used.
Advantages of BMMM
  Decreases multicast request completion time
  Prevents ACK and CTS collisions
  Reduces the number of contention phases from n to 1

## Slide 12: Connectivity-Based Reliable Multicast MAC Protocol for IEEE 802.11 Wireless LANs
Improvisation of BMMM
Reduces RAK transmissions
AP finds a sequence(Q) of n recipients in u sequentially connected i.e each recipient except the first one can hear its previous recipient in the sequence
AP polls the sequence by transmitting a single RAK frame including MAC of all nodes in the sequence
In response all the recipients transmit their ACKs (on which uplink data is piggy-backed) after a SIFS interval
If the AP does not receive an ACK from some node. It sends another RAK to the node and the sequence following it.
The problem of finding the minimum number of nodes is modelled as the traveling salesman problem

## Slide 13
Sequence of 4 nodes , where three nodes can overhear the transmission to the first node

## Slide 14: REMP (Reliable and Efficient Multicast Protocol)
Leader-Based Protocol
Node with the lowest RSSI is selected as the leader
Leader sends Block acknowledgements
In case of loss
  Non-leaders send negative-ACKs
  All the nodes then send block-ACKs with their respective RSSI values
  Based on these RSSI values a new leader is selected
Overhead of leader Selection process

## Slide 15: DPMM (Double Piggy-back Mode Multicast)
ACK frame is piggy-backed in CTS frame
ACK for the last packet is explicitly sent
Allows multicast frame aggregation by adding a bitmap to the CTS frame
Priority information is piggybacked in multicast data frames to avoid collisions with CTS frames
Cluster-Head(CH) mechanism to improve performance
  Selection done at AP to reduce overhead
  Control packets only sent by CHs
  CH selected in case of more than 3 nodes
  Several CHs are selected by AP

## Slide 16: Cluster-Head Selection in DPMM
IGMP is used to generate group membership report
“group join” and “group leave” messages are sent by terminals to the AP
Link conditions are estimated by these IGMP messages
Depending on the link-conditions clusters are divided into groups
Nodes with similar link conditions are grouped into one cluster
CHs within clusters are chosen in a Round Robin fashion

## Slide 17
DPMM
High overhead due to CTS frames
Higher unicast throughput
REMP
Less overhead as ACK is only sent by leader
Higher Multicast throughput
Less delay as AP retransmits to only three nodes i.e the cluster heads
Slightly higher delay as AP retransmits to all the multicast nodes
More Reliable as response is taken from all the nodes in case of lost packets
Less Fair as only the 3 CHs are responsible for NACK/ACK

## Slide 18: Approaching the problem
Tradeoff between reliability and performance
  Higher reliability -> Increased feedback -> Increased overhead
  Higher Performance -> Decreased overhead -> Decreased reliability
Our Goal: Maximize performance while incurring minimum overhead
  Obtain feedback passively
  Design an efficient rate control mechanism utilizing gathered feedback

## Slide 19: Passively Obtaining Feedback
Feedback always available at higher layers
We Propose specializing for Real Time Protocol
  RTP Packets contain sequence number
  Each video stream requires control connection
  Feedback transmitted over control connection
Snooping on these packets alternative to explicit Acknowledgements

## Slide 20: Reducing Performance Overhead
Previously illustrated problem due to receivers with different link quality
Split Receivers into separate groups according to link quality
Use different transmission rates for each group

## Slide 21: Thank You