## Slide 1: Design of an Efficient Multicast Protocol for IEEE 802.11n WLANs
Ahmed Mehfooz, Amna Abid, Shanzae Nadeem Khan

## Slide 2: Background Motivation
Multicast is an efficient way to broadcast a single packet to multiple receivers – unnecessary packet duplications are avoided.
Multicast has some limitations:
  Packets only sent on base rate – low overall throughput
  Not reliable due to the absence of a feedback mechanism
  Inefficient due to lack of frame aggregation since no feedback available
Tradeoff between reliability and performance
  Higher reliability -> Increased feedback -> Increased overhead
  Reduced feedback -> Decreased overhead -> Improved performance
Our Goal: Maximize performance while incurring minimum overhead

## Slide 3: Milestones: Fall Semester
Month | Deliverable
October | Literature Review Brainstorming on possible solutions
November | Driver Code Evaluation Test-Bed Setup Experiments to Evaluate stock 802.11n Multicast Performance
December | Exploring for the most viable method to passively get feedback from receivers. Will require extensive experiments on the test-bed and driver code analysis. (Proved unsuitable – new approach needed to be adopted.)

## Slide 4: Milestones: Spring Semester
Month | Deliverable
February | Developing a viable feedback mechanism to provide rate control for multicast transmissions using hooking.
March | Developing the Rate Adaptation Protocol using probing.
April | Developing the Leader Selection Protocol using the ACK overhearing method.
May | Carrying out experiments to observe the magnitude of improvement in multicast transmissions by implementing the aforementioned protocols in multicast 802.11.

## Slide 5: Experiments to evaluate stock 802.11 multicast performance

## Slide 6: Implementing a Viable Feedback Mechanism
Hooking – method of code injection in an active LINUX kernel
Our Hook:
  Sits between the Physical Layer and Wireless Driver
  Intercepts packets associated with a single multicast group
  Periodic feedback response from the receivers containing PER and RSSI values
Entire packet must be manually crafted – requires meticulous handling of fields e.g. MAC Addresses and IP Addresses

## Slide 7: How the kernel module works:
Hook Registered
Does the Dest. IP Address of the packet match the address of our multicast group?
Send Feedback
Craft UPD Header
Craft IP Header
Craft Ethernet Header
Handover Packet to Driver for Transmission Using dev_queue_xmit()
Add Feedback Information

## Slide 8: Client Module

## Slide 9: Server Module

## Slide 10: Rate Adaptation Algorithm

## Slide 11: Experimental Setup
Tested our protocol in three different scenarios with varying signal strengths:
  High signal
  Medium signal
  Low signal

## Slide 12: Future Venues

## Slide 13: Leader Selection Protocol (The Topology)
Novelties:
  New method of Leader Selection
  Entirely distributed – no dependence on the AP

## Slide 14: Leader Selection Protocol (The Algorithm)

## Slide 15: Future Venues
Split Receivers into separate groups according
to link quality
  Use different transmission rates for each group
Further optimization of the Leader Selection Protocol
  Increased Scalability
  Dealing with the Hidden Node Problem – Implicit overhearing of the leader’s ACKs by any distant node
Further optimization of the Kernel Module
  Directly utilizing MAC Layer ACKs instead of UDP sockets for sending feedback

## Slide 16: Related Works
Multicast
Protocols
Leader-based
SRM(Semi Reliable Multicasting)
ACK-Based
Non-leader-Based
ACK-Based
NACK-Based
NACK-Based
REMP(Reliable and efficient Multicast Protocol)
DPMM(Double Piggyback Mode Multicast)
Adaptive Multicast Services
(e.g.)
(e.g.)
(e.g.)
(e.g.)

## Slide 17: Thank You