## Slide 1: Design of an Efficient Multicast Protocol for IEEE 802.11 WLANs
Ahmed Mehfooz, Amna Abid, Shanzae Nadeem Khan

## Slide 2: Background Motivation
Multicast is an efficient way to broadcast a single packet to multiple receivers – unnecessary packet duplications are avoided.
Multicast has some limitations:
  Packets only sent on base rate – low overall throughput
  Not reliable due to the absence of a feedback mechanism
  Inefficient due to lack of frame aggregation since no feedback available
Tradeoff between reliability and performance
  Higher reliability -> Increased feedback -> Increased overhead
  Reduced feedback -> Decreased overhead -> Improved performance
Our Goal: Maximize performance while incurring minimum overhead

## Slide 3: Experiments to evaluate stock 802.11 multicast performance

## Slide 4: Milestones: Fall Semester
Month | Deliverable
October | Literature Review Brainstorming on possible solutions
November | Driver Code Evaluation Test-Bed Setup Experiments to Evaluate stock 802.11 Multicast Performance
December | Exploring for the most viable method to passively get feedback from receivers. Will require extensive experiments on the test-bed and driver code analysis. (Proved unsuitable – new approach needed to be adopted.)

## Slide 5: Milestones: Spring Semester
Month | Deliverable
February | Developing a viable feedback mechanism to provide rate control for multicast transmissions using hooking.
March | Developing the Rate Adaptation Protocol using probing.
April | Developing the Leader Selection Protocol using the ACK overhearing method.
May | Carrying out experiments to observe the magnitude of improvement in multicast transmissions by implementing the aforementioned protocols in multicast 802.11.

## Slide 6: Implementing a Viable Feedback Mechanism
Hooking – method of code injection in an active LINUX kernel
Our Hook:
  Sits between the Physical Layer and Wireless Driver
  Intercepts packets associated with a single multicast group
  Periodic feedback response from the receivers containing PER values

## Slide 7: How the kernel module works:
Hook Registered
Does the Dest. IP Address of the packet match the address of our multicast group?
Send Feedback
Craft UPD Header
Craft IP Header
Craft Ethernet Header
Handover Packet to Driver for Transmission Using dev_queue_xmit()
Add Feedback Information

## Slide 8: Rate Adaptation Mechanism
A viable feedback available to choose the optimum rate for multicast transmissions
A Rate Adaptation Algorithm implemented in the Kernel Module running on the Server
  Utilizes feedback from the client for every rate index
  Picks best rate for next transmission based on projected throughput
  Occasional backward and forward probing

## Slide 9: Rate Adaptation Mechanism (The Algorithm)

## Slide 10: Leader Selection Protocol (The Topology)
Novelties:
  Previous leader selection protocols impose a very high overhead
  Our approach randomly assigns leader initially
  Subsequent leader corrections in a distributed manner

## Slide 11: Leader Selection Protocol (The Algorithm)

## Slide 12: Experimental Evaluation (The Test-Bed Topologies)

## Slide 13: Experimental Evaluation (The Results!)

## Slide 14: Experimental Evaluation (The Results!)

## Slide 15: Experimental Evaluation (The Results!)

## Slide 16: Future Venues
Split Receivers into separate groups according
to link quality
  Use different transmission rates for each group
Further optimization of the Leader Selection Protocol
  Increased Scalability
  Dealing with the Hidden Node Problem – Implicit overhearing of the leader’s ACKs by any distant node
Further optimization of the Kernel Module
  Directly utilizing MAC Layer ACKs instead of UDP sockets for sending feedback

## Slide 17: Related Works
Multicast
Protocols
Leader-based
SRM(Semi Reliable Multicasting)
ACK-Based
Non-leader-Based
ACK-Based
NACK-Based
NACK-Based
REMP(Reliable and efficient Multicast Protocol)
DPMM(Double Piggyback Mode Multicast)
Adaptive Multicast Services
(e.g.)
(e.g.)
(e.g.)
(e.g.)

## Slide 18: Thank You