## Slide 1: 802.11 Multicast Protocols

## Slide 2: Introduction
Two main categories
  ACK Based
  NAK Based

## Slide 3: ACK Based - DPMM(Double piggy back mode multicast)
Positive feedback based multicast MAC protocol.
Control overheads are avoided by piggy backing the ACKs in CTS.
Collisions of control messages(CTS) are avoided by assigning priority to the nodes.
Multicast frame aggregation is made efficient by using bitmap in CTS.

## Slide 4: DPMM
Not scalable.
CTS/RTS overhead.

## Slide 5: NAK Based Multicast Protocols
Rely on negative feedback incase of data loss
Requires less channel resources so more scalable
Data loss more likely
NAK implosion also possible

## Slide 6: REMP
Incorporates block acks within a NAK based protocol, therefore efficient utilization of frame aggregation
Requires RSSI feedback from all participants
Requires initial leader selection and reselection upon packet loss
Error recovery mechanism has a high overhead which may not be suitable for applications such as video streaming

## Slide 7: Transparent Multicast Unicast Translation
Translates and Copies Multicast Packets into multiple Unicast Packets at the MAC layer
Uses a Multicast Unicast Translator (MUT) – MAC Layer Entity
MUT transparently duplicates a multicast packet and changes the destination MAC address of each copy to each receiver and then forwards the copies to the wireless LAN segment

## Slide 8: Pros
Enables higher transmission rates
Reduces media occupation freeing up resources for other transmissions
Enables retransmission function enabling recovery of lost frames – reliability improves
Feasible since only MAC header and IP header are changed

## Slide 9: Cons
Translation overhead
Scalability Issue
More load on the medium