## Slide 1: Design of Efficient Multicast Protocol for IEEE 802.11n WLANs

## Slide 2: Why Multicast?
Some applications require multiple copies of the same packet
For example: Live Video Streaming
Unicast transmission proves to be inefficient
Multicast concurrently broadcasts one packet to multiple destinations – an efficient alternative to reduce unnecessary packet duplications

## Slide 3: Problems Posed by Multicast in 802.11n
Low Transmission Rates
Poor Reliability because of lack of ACKs
Frame Aggregation not supported

## Slide 4: Related Work
Existing Protocols
Leader-based
SRM(Semi Reliable Multicasting)
ACK-Based
Non-leader-Based
ACK-Based
NACK-Based
NACK-Based
REMP(Reliable and efficient Multicast Protocol)
DPMM(Double Piggyback Mode Multicast)
Adaptive Multicast Services

## Slide 5: Leader-Based Multicast Protocols
Leader Selection
  Based on channel conditions(usually the node with the worst channel conditions is chosen)
  Done in a Round Robin fashion.
Leader is responsible for sending CTS and ACKs on behalf of the group.
Other nodes remain silent or send NACK in case of loss.

## Slide 6: Problems with Leader-Based approach
A new Leader is Selected when
  A new node joins the group
  A leader node leaves the group
  Channel conditions change
  A loss occurs
  Leader Selection becomes difficult in case of varying Network Conditions and has a constant overhead.

## Slide 7: REMP
Elects Leader for a Multicast group who is responsible for replying with Block Acknowledgements, this makes frame aggregation possible
Leader is always the node with weakest signal
Non-Leaders respond with NAKs to alert sender with packet loss on their end
Requires blockAcks from every node incase a NAK is received and a fresh round of leader selection

## Slide 8: Thoughts…
Error recovery mechanism has a high overhead which may not be suitable for applications such as video streaming
An improvement that comes to mind may be to divide the receivers into groups: Slow and Fast

## Slide 9: Thank You